# SAFE OPERATING PROCEDURE

Belt Sander

|  | DO NOT use this power tool unless you have had instruction and training in its safe use and operation. Teacher permission MUST be given to operate this power tool. |
| --- | --- |
| The risk of injury when using this machine is SUBSTANTIAL |

## IDENTIFIED RISKS AND HAZARDS

Hazards that may arise when operating portable sander equipment include:

- moving and rotating parts (rollers and belt)

- movement of the workpiece

- inhalation of dust particles

- electrocution from power faults, faulty equipment or incorrect use

- burns and abrasions sanding belt

### PRE-OPERATIONAL SAFETY

- Before using the Belt sander, examine the power cord, extension lead, plugs, sockets and power outlet for damage.

- Before starting the Belt sander ensure that the sanding belt is correctly fitted.

- Do not use a blunt or damaged sanding belt.

- Always inspect the workpiece to ensure that there aren't any items which might damage the sanding belt or cause injury to the operator.

- Secure and support the workpiece using clamps, bench vices or appropriate weights.

#### OPERATING SAFETY PRECAUTIONS

- Keep fingers and hands clear of moving parts and the sanding belt.

- Ensure that material being worked on is well supported or held securely where necessary.

- When the Belt sander has reached the operating speed, apply the load gradually.

- Avoid blocking or covering the motor ventilation slots while using the Belt sander.

- Do not strain power cords or extension leads, especially by lifting or dragging Belt sanders by the cords, or by pulling on the cord to remove the plug from the power outlet.

- Always position electrical cords with care to avoid trip hazards and to prevent damage to the cord or extension lead.