# SAFE OPERATING PROCEDURE

Abrasive Saw

|  | DO NOT use this power tool unless you have had instruction and training in its safe use and operation. Teacher permission MUST be given to operate this type of machinery. |
| --- | --- |
| The risk of injury when using this machine is VERY HIGH |

## IDENTIFIED RISKS AND HAZARDS

Hazards that may arise when operating the angle grinder include:

- moving and rotating parts (blades, bits& tool disintegration)

- movement of the work piece

- inhalation of dust particles

- electrocution from power faults or faulty equipment

- burns from hot materials or friction

- ejection of waste materials from cutting blades, discs & cutters

- mutilation of body parts if control is compromised

### PRE-OPERATIONAL SAFETY

- Before using the any power tool, examine the power cord, extension lead, plugs, sockets and power outlet for damage.

- Before starting the grinder ensure that the wheel, guards and attachments are secure and correctly fitted.

- Do not use blunt or damaged grinding wheels.

- Always inspect the work piece to ensure that there aren't any items which might damage the grinding wheel or cause injury to the operator.

#### OPERATING SAFETY PRECAUTIONS

- Keep fingers and hands clear of the grinding wheel.

- Always keep the power cord clear of the wheel and workpiece.

- Ensure that material being worked on is well supported or held securely.

- Ensure that off-cuts cannot fall onto the feet of the operator.

- Never make adjustments while the grinder is running.

- Do not switch off the grinder when it is under load, except in an emergency.

- Always allow the grinder to reach operating speed before using it on the work piece. When the grinder has reached the operating speed apply the load gradually.