# SAFE OPERATING PROCEDURE

Angle Grinder

|  | DO NOT use this power tool unless you have had instruction and training in its safe use and operation. Teacher permission MUST be given to operate this type of machinery. |
| --- | --- |
| The risk of injury when using this machine is VERY HIGH |

## IDENTIFIED RISKS AND HAZARDS

Hazards that may arise when operating the angle grinder include:

- moving and rotating parts (blades, bits& tool disintegration)

- movement of the work piece

- inhalation of dust particles

- electrocution from power faults or faulty equipment

- burns from hot materials or friction

- ejection of waste materials from cutting blades, discs & cutters

- mutilation of body parts if control is compromised

### PRE-OPERATIONAL SAFETY

- Before using the any power tool, examine the power cord, extension lead, plugs, sockets and power outlet for damage.

- Before starting the grinder ensure that the wheel, guards and attachments are secure and correctly fitted.

- Do not use blunt or damaged grinding wheels.

- Always inspect the work piece to ensure that there aren't any items which might damage the grinding wheel or cause injury to the operator.

#### OPERATING SAFETY PRECAUTIONS

- Keep fingers and hands clear of the grinding wheel.

- Always keep the power cord clear of the wheel and workpiece.

- Ensure that material being worked on is well supported or held securely.

- Ensure that off-cuts cannot fall onto the feet of the operator.

- Never make adjustments while the grinder is running.

- Do not switch off the grinder when it is under load, except in an emergency.

- Always allow the grinder to reach operating speed before using it on the work piece. When the grinder has reached the operating speed apply the load gradually.

To operate this machine/equipment you MUST have:

- Read and understood the Safe Working Procedure

- Completed the Safe Work Test with a 100% score

- Demonstrated competent and safe use

# Text boxes

- Very High risk of injury to the operator or other persons if the procedures in this activity are not carried out in the proper manner

- An injury sustained during this activity could result in a permanent physical disability or  even death

- Teacher approval is required to operate the equipment or proceed with this activity and close direct supervision (next to the safety zone) by the teacher is required

- Appropriate PPE will be required to further reduce the risk of injury

## Risk of Injury

is

# VERY HIGH

# Level

5