# SAFE OPERATING PROCEDURE

Bandsaw

|  | DO NOT use this machine unless you have had instruction and training in its safe use and operation. Teacher permission MUST be given to operate this machine. |
| --- | --- |
| The risk of injury when using this machine is HIGH |

## IDENTIFIED RISKS AND HAZARDS

Hazards that may arise when operating the Bandsaw include:

- moving and rotating parts (blades and bits, tool disintegration)

- movement of the workpiece

- hand and finger injuries from rotating blades, spindles or pulleys

- electrocution from equipment or cords

- inhalation of dusts

## noise from high speed blade

### PRE-OPERATIONAL SAFETY

- The isolating switch should be in the OFF position when adjusting, maintaining and repairing the Bandsaw.

- The thrust wheels and guides should be in good condition, correctly adjusted and should rotate firmly.

- The upper guide assembly should be adjusted as close as practicable to the work.

- The table insert, if fitted should be in good condition and free of small off-cuts which may lodge between the blade and insert.

- The blade should be sharp, undamaged and set correctly.

- The blade type should be suited to the material to be cut.

- The blade should be tensioned correctly and tracking properly.

- The work area should be clean and free of off-cuts, saw dust and other obstacles.

- If an extraction system is fitted it should be operating correctly and free of obstructions.

#### OPERATING SAFETY PRECAUTIONS

- Off-cuts and saw dust must not be removed from the table with the hands while the blade is moving.

- Never attempt to cut curves that are too tight for the width of blade in the bandsaw.

- A push stick should be used wherever possible to ensure the hands are kept away from the blade.

- Avoid backing out the material from the blade when making long cuts.

- Excessive pressure on the blade can cause it to break.