# SAFE OPERATING PROCEDURE

Battery Drill

|  | DO NOT use this cordless tool unless you have had instruction and training in its safe use and operation. Teacher permission MUST be given to operate this cordless tool. |
| --- | --- |
| The risk of injury when using this machine is LOW |

## IDENTIFIED RISKS AND HAZARDS

Hazards that may arise when operating the battery drill include:

- moving and rotating parts (drill bits and chuck)

- movement of the workpiece

- inhalation of fumes and dust particles

- ejection of waste materials from cutting blades

- burns from hot materials or friction

## PRE-OPERATIONAL SAFETY

- Before using the battery drill, examine the casing for damage.

- Do not use blunt or damaged drill bits.

- Do not test drill bits for sharpness with the fingers.

- Always inspect the workpiece to ensure that there aren't any items which might damage the drill bit or cause injury to the operator.

- Secure and support the workpiece using clamps, bench vices or appropriate weights.

## OPERATING SAFETY PRECAUTIONS

- Keep fingers and hands clear of the drill bit.

- Never make adjustments while the battery drill is running.

- When the drill bit has reached the operating speed, apply the load gradually.

- Avoid blocking or covering the motor ventilation slots while using the battery drill.

- Never drill pieces of material by holding them in the hands.

- Hold the drill firmly and exert care when the drill bit begins to break through the workpiece

- Never operate the charger with a damaged cord or plug.

- Be aware not to operate the charger anywhere near water.