# SAFE OPERATING PROCEDURE

Belt Linishing Machine

|  | DO NOT use this machine unless you have had instruction and training in its safe use and operation. Teacher permission MUST be given to operate this machine. |
| --- | --- |
| The risk of injury when using this machine is MODERATE |

## IDENTIFIED RISKS AND HAZARDS

Hazards that may arise when operating the belt linisher include:

- movement of the workpiece

- inhalation of dust particles

- electrocution from power faults, faulty equipment or incorrect use

- burns from hot materials or friction

- hand and finger injuries from rotating sanding belt

- squash, pinch and crush injuries

### PRE-OPERATIONAL SAFETY

- Check that the dust extraction system is working properly.

- Check the condition of the sanding pad and ensure that all guards are correctly fitted and secured.

- Check the condition of the abrasive and the join in the belt. Also examine the belt for nicks or tears on the edges. Check the belt tension and tracking.

- Ensure that the abrasive belt grade is the correct one for the sanding job.

- Check that the belt has been installed properly, with the join in the correct position relative to the belt rotation.

#### OPERATING SAFETY PRECAUTIONS

- The isolating switch should be in the OFF position when adjusting, maintaining and repairing the Belt Linisher. The Linisher must be isolated from the main electricity supply.

- Never stand in a direct line with the abrasive belt when the machine is running.

- Allow the belt to reach maximum speed before applying sanding pressure.

- Make sure that the workpiece rests flat on the sanding table at all times.

- Keep the hands well away from the abrasive belt when the sander is running.

- When the sanding operation is finished, switch the linisher off and wait for the belt to become stationary before leaving the work area.

# Text boxes

PLACE A PICTURE OF YOUR MACHINE or TOOL HERE