# SAFE OPERATING PROCEDURE

Bench/Pedestal Drill

|  | DO NOT use this machine unless you have had instruction and training in its safe use and operation. Teacher permission MUST be given to operate this machine. |
| --- | --- |
| The risk of injury when using this machine is MODERATE |

## IDENTIFIED RISKS AND HAZARDS

Hazards that may arise when operating the drilling machine include:

- movement of the workpiece

- inhalation of dust particles

- ejection of waste materials from cutting blades

- hand and finger injuries from rotating drills, spindles or pulleys

- electrocution from equipment or cords

- squash, pinch and crush injuries

### PRE-OPERATIONAL SAFETY

- The isolating switch should be in the OFF position. The machine must be isolated from the main electricity supply when not in use.

- Check that drill speed is suitable for the work to be done and adjust as required.

- Check the condition of the drill bits. They should be kept sharp at all times and free of burrs on the shank.

- All guards should be correctly fitted and secured.

- Check all adjustments and settings carefully before commencing any drilling or boring operations.

- The drilling machine and work area should be clean and free of wood chips and other obstacles.

#### OPERATING SAFETY PRECAUTIONS

- If the machine is not fitted with a keyless chuck, tighten the chuck uniformly when the drill is inserted and always use the correct size chuck key.

- Remove the key from the chuck before starting the drill press.

- Allow the drill bit to cut at its own speed without applying excessive pressure.

- Irregular shaped work should be securely held in a jig, vice or clamp.

- Seek assistance when handling long lengths of timber or sheets.

- Keep the hands clear of the drill bit when the drilling machine is operating.

- Do not remove waste material from the drilling table while the machine is operating.