# SAFE OPERATING PROCEDURE

Bench/Pedestal Grinder

|  | DO NOT use this machine unless you have had instruction and training in its safe use and operation. Teacher permission MUST be given to operate this machine. |
| --- | --- |
| The risk of injury when using this machine is SUBSTANTIAL |

## IDENTIFIED RISKS AND HAZARDS

Hazards that may arise when operating the grinder include:

- moving and rotating parts (wheel disintegration)

- movement of the workpiece

- inhalation of dust particles

- electrocution from power faults or faulty equipment

- burns from hot materials or friction

- hand and finger injuries from rotating wheels

- noise

### PRE-OPERATIONAL SAFETY

- The isolating switch should be in the OFF position. The grinding machine must be isolated from the main electricity supply when not in use.

- Check that the abrasive wheel is suitable for the workpiece to be grinded.

- Check the condition of the abrasive wheel. It should be kept in good condition at all times and free of cracks or chips.

- All guards and shields must be correctly fitted and secured.

- Check all adjustments and tool rest settings carefully before commencing any grinding operation.

- The grinding machine and work area should be clean and free of scrap and other obstacles.

#### OPERATING SAFETY PRECAUTIONS

- Off-cuts and metal swarf must not be removed from the tool rest with the hands when the wheel is rotating.

- The operator should never stand directly in line with the grinding wheel.

- The workpiece should never be forced into the wheel.

- The grinder should never be left unattended with the power switched on.