# SAFE OPERATING PROCEDURE

Metal Cutting Bench Shears

|  | DO NOT use this machine unless you have had instruction and training on its safe use and operation. Teacher permission MUST be given to operate this machine. |
| --- | --- |
| The risk of injury when using the Bench Shears is MODERATE |

## IDENTIFIED RISKS AND HAZARDS

Hazards that may arise when operating the metal cutting bench shears include:

- moving blade

- movement of the workpiece

- ejection of waste material from the cutting process

- hand and finger injuries from sharp edges

- squash, pinch and crush injuries

- manual handling of large sheets of sheetmetal

### PRE-OPERATIONAL SAFETY

- Check the condition of the blade on the bench shears and check that the top blade and handle assembly are not loose.

- Make sure that the hold down is positioned correctly to prevent the metal from kicking up when shearing pressure is applied.

#### OPERATING SAFETY PRECAUTIONS

- Make sure all other students keep outside the safety zone at all times.

- Wear PPE such as safety spectacles when using the bench shears to protect your

eyes.

- Do not wear loose clothing, especially long sleeves and neck ties.

- Make sure the hands are well clear of the hold down and cutting blade.

- Make sure that no one is behind and in line with the handle of the bench shears

when they are pulled down to cut the material.

- Never attempt to cut round material using the straight blades of the bench shears.

- Use the hole in the cutting blades of the bench shears to cut round stock.

- Seek assistance when cutting large sheets of metal.

- Always clean up the offcuts and scrap after the cutting procedure.

# Text boxes

PICTURE OF YOUR MACHINE or TOOL HERE