# SAFE OPERATING PROCEDURE

Compressed Air Equipment

|  | DO NOT use this equipment unless you have had instruction and training in its safe use and operation. Teacher permission MUST be given to operate this equipment. |
| --- | --- |
| The risk of injury when using this machine is HIGH |

## IDENTIFIED RISKS AND HAZARDS

Hazards that may arise when operating air operated machinery include:

- moving and rotating parts (blades and bits, tool disintegration)

- inhalation of fumes and dust particles

- electrocution from power faults, faulty equipment or incorrect use

- ejection of waste materials from cutting blades

- burns from hot materials or friction

- hand and finger injuries from rotating blades, spindles or pulleys

- noise

### PRE-OPERATIONAL SAFETY

The following safety checks should be carried out when preparing to set up, operate or maintain an air compressor and associated equipment:

- Always check that the air hoses are in good working order and the hose connections fit correctly before switching on the compressor.

- Check the condition of the air tools and equipment to be used.

- The compressor relief valve should be checked regularly and the air receiver needs to be checked for accumulation of water.

- All guards should be correctly fitted and secured.

- Check all adjustments and settings carefully before commencing any operation.

#### OPERATING SAFETY PRECAUTIONS

- Do not point the air nozzle towards the body, especially the face.

- Make sure all air attachments and air hoses are kept clear of the working parts of

the compressor.

- The guard on the compressor’s pulley and belt system must never be removed.

- When spraying paints or solvents, the operator must wear Personal Protective

Equipment such eye spectacles and spray mask.

- Make sure there is adequate ventilation in the spray painting area, to prevent a

dangerous build up of vapour.