# SAFE OPERATING PROCEDURE

Disc Sanding Machine

|  | DO NOT use this machine unless you have had instruction and training in its safe use and operation. Teacher permission MUST be given to operate this machine. |
| --- | --- |
| The risk of injury when using this machine is MODERATE |

## IDENTIFIED RISKS AND HAZARDS

Hazards that may arise when operating the disc sander include:

- moving and rotating parts

- movement of the workpiece

- inhalation of dust particles

- burns from hot materials or friction

- hand and finger injuries from rotating wheel

- electrocution from equipment or cords

### PRE-OPERATIONAL SAFETY

- The isolating switch should be in the OFF position. The machine must be isolated from the main electricity supply when not in use.

- The work area should be clean and free of dust and other obstacles.

- The table should move freely and be free of all material except the workpiece.

- Check that the dust extraction system is working properly.

- Ensure all guards are correctly fitted and secured.

- Check the condition of the abrasive on the disc. Also examine the disc for uneven wear and for nicks or tears on the edges.

- Ensure that the disc is the correct one for the sanding operation.

#### OPERATING SAFETY PRECAUTIONS

- Ensure that the workpiece rests flat on the table at all times.

- Allow the disc to reach maximum speed before applying sanding pressure.

- Never stand in a direct line with the face of the disc when the machine is running.

- Keep hands well away from the abrasive disc when the machine is running.

- When the sanding operation is finished, switch the sander off and wait till the disc is stationary before leaving the work area.