# SAFE OPERATING PROCEDURE

Drop Saw

|  | DO NOT use this machine unless you have had instruction and training in its safe use and operation. Teacher permission MUST be given to operate this machine. |
| --- | --- |
| The risk of injury when using this machine is VERY HIGH |

## IDENTIFIED RISKS AND HAZARDS

Hazards that may arise when operating the drop saw include:

- movement of the workpiece

- electrocution from power faults, faulty equipment or incorrect use

- ejection of waste materials from cutting blades

- hand and finger injuries from rotating blades, spindles or pulleys

- inhalation of dusts

- noise from high speed cutters

### PRE-OPERATIONAL SAFETY

- The isolating switch should be kept in the OFF position while the saw is not being used. The saw must be isolated from the main electricity supply.

- The blade should be fitted with the teeth facing in the direction of the blade rotation.  This holds the material against the fence during the cutting operation.

- The blade should be sharp, undamaged and square to the table for docking operations.

- Guards must be fitted, correctly adjusted, secured where necessary or be rotating freely depending on the machine.

- The fence should be square to the table and locked in position where necessary.

#### OPERATING SAFETY PRECAUTIONS

- The operator should never stand directly in line with the saw blade.

- The saw should be operated with the hand that does not require the operator's body to be in line with the blade.

- The blade should never be forced into the material. Allow the blade to cut at its own speed.

- The saw should always be returned to a non-cutting position after each cut is made. The saw should never be left unattended with the power switched on.

- Material should never be left on the table away from the fence and in line with the saw blade.

- Off-cuts and saw dust must not be removed from the table with the hands when the blade is rotating.