# SAFE OPERATING PROCEDURE

Portable Electric Drill

|  | DO NOT use this power tool unless you have had instruction and training in its safe use and operation. Teacher permission MUST be given to operate this power tool. |
| --- | --- |
| The risk of injury when using this machine is SUBSTANTIAL |

## IDENTIFIED RISKS AND HAZARDS

Hazards that may arise when operating portable electric drill include:

- moving and rotating parts (bits, tool disintegration)

- movement of the workpiece

- inhalation of fumes and dust particles

- electrocution from power faults, faulty equipment or incorrect use

- ejection of waste materials from cutting blades

- burns from hot materials or friction

### PRE-OPERATIONAL SAFETY

- Before using the electric drill, examine the power cord, extension lead, plugs, sockets and power outlet for damage.

- Do not use blunt or damaged drill bits.

- Always inspect the workpiece to ensure that there aren't any items which might damage the drill bit or cause injury to the operator.

- Secure and support the workpiece using clamps, bench vices or appropriate weights.

#### OPERATING SAFETY PRECAUTIONS

- Keep fingers and hands clear of the drill bit.

- Never operate electric drills in wet or damp conditions.

- Always keep the power cord clear of moving parts and the drill bit.

- Allow the electric drill to reach operating speed before using it on the workpiece.

- Wear appropriate Personal Protective Equipment such as safety glasses for eye protection.

- Always position electrical cords with care to avoid trip hazards and to prevent damage to the cord or extension lead.

- Hold the drill firmly using both hands and exert care when the drill bit begins to break through the workpiece.