# SAFE OPERATING PROCEDURE

Jigsaw

|  | DO NOT use this power tool unless you have had instruction and training in its safe use and operation. Teacher permission MUST be given to operate this power tool. |
| --- | --- |
| The risk of injury when using this machine is MODERATE |

## IDENTIFIED RISKS AND HAZARDS

Hazards that may arise when operating power jigsaw equipment include:

- moving and reciprocating blade

- movement of the workpiece

- inhalation of dust particles

- electrocution from power faults, faulty equipment or incorrect use

- burns from hot materials or friction

## PRE-OPERATIONAL SAFETY

- Before using the jigsaw, examine the power cord, extension lead, plugs, sockets and power outlet for damage.

- Before you start cutting ensure that the cutting blade, fences, guides and any attachments are secure and correctly fitted.

- Do not use blunt or damaged cutting blades.

- Always inspect the workpiece to ensure that there aren't any items which might damage the cutting tool or cause injury to the operator.

- Secure and support the workpiece using clamps, bench vices or appropriate weights.

## OPERATING SAFETY PRECAUTIONS

- Never operate jigsaws in wet or damp conditions.

- Keep fingers and hands clear of the cutting blade.

- Always keep the power cord clear of moving parts and the cutting blade.

- Ensure that off-cuts cannot fall onto the feet of the operator.

- When the jigsaw has reached the operating speed, apply the load gradually.

- Avoid awkward hand positions where a sudden slip could cause finger injury.

- While cutting the foot plate should rest wholly on the workpiece.

- Avoid forcing or feeding the Jigsaw too fast into the material.

- Always position electrical cords with care to avoid trip hazards and to prevent

damage to the cord or extension lead.