# SAFE OPERATING PROCEDURE

Magnabend Folding Machine

|  | DO NOT use this machine unless you have had instruction and training in its safe use and operation. Teacher permission MUST be given to operate this machine. |
| --- | --- |
| The risk of injury when using this machine is MODERATE |

## IDENTIFIED RISKS AND HAZARDS

Hazards that may arise when folding sheetmetal with a Magnabend include:

- electric shock from faulty electrical equipment

- cuts from sheetmetal

- finger damage from the clamp bar

### PRE-OPERATIONAL SAFETY

- Before using the magnabend folder, examine the power cord, extension lead, plugs, sockets and power outlet for damage. Look for:

- cracked or damaged casing

- bare wires or loose connections

- damage to cord sheathing

- loose or missing screws

- Secure and support the workpiece using the supplied clamps only.

- Ensure that there are no flammable gases, liquids or other materials in the work area.

- Make sure the floor area is not untidy with metal offcuts.

#### OPERATING SAFETY PRECAUTIONS

- Ensure the full length clamp bar is positioned on the machine.

- Make sure the lifting balls on the ends of the clamp bar are resting in the locating grooves and adjust the eccentric adjustors at either end of the clamp bar.

- Insert the workpiece and align the bend line, before slightly tilting the bending bar up with one hand while pressing and holding the green start button with the other hand.

- After applying this pre-clamping pressure, use the other hand to grab the other handle and continue to bend upwards until the required angle is reached.

- Never attempt to use the clamp bars on their edge or attempt to hold the clamp bars with the hands while switching on the machine.

- Allow the Magnabend folder to cool down for 30 minutes if the thermal overload switch is tripped due to the machine being in the fully clamped state continuously.

# Text boxes

PLACE A PICTURE OF YOUR MACHINE or TOOL HERE