# SAFE OPERATING PROCEDURE

Portable Router (Plunge Type)

|  | DO NOT use this power tool unless you have had instruction and training in its safe use and operation. Teacher permission MUST be given to operate this power tool. |
| --- | --- |
| The risk of injury when using this machine is SUBSTANTIAL |

## IDENTIFIED RISKS AND HAZARDS

Hazards that may arise when operating the plunge router include:

- moving and rotating parts (bits and tool disintegration)

- movement of the workpiece

- inhalation of dust particles

- electrocution from power faults, faulty equipment or incorrect use

## PRE-OPERATIONAL SAFETY

- Before using the router, examine the power cord, extension lead, plugs, sockets and power outlet for damage.

- Check the router bit carefully for cracks or damage before installing it into the router spindle.

- Always inspect the workpiece to ensure that there aren't any items which might damage the bit or cause injury to the operator.

- Secure and support the workpiece using clamps or bench vices.

## OPERATING SAFETY PRECAUTIONS

- Keep fingers and hands clear of moving parts and the rotating bit.

- Always keep the power cord clear of moving parts and the rotating bit.

- Ensure that material being worked on is well supported or held securely where necessary.

- Do not strain the power cord especially by lifting or dragging the router by the cord, or by pulling on the cord to remove the plug from the power outlet.

- Never operate Routers in wet or damp conditions.

- Hold the router firmly with both hands and keep the hands and fingers away from the rotating spindle and router bit.

- Watch for vibration or wobbling as this could indicate an improperly installed router bit.

- Do not leave the Router running unattended.

- Always position electrical cords with care to avoid trip hazards and to prevent damage to the cord or extension lead.