# SAFE OPERATING PROCEDURE

Wood Thicknesser

|  | DO NOT use this machine unless you have had instruction and training in its safe use and operation. Teacher permission MUST be given to operate this machine. |
| --- | --- |
| The risk of injury when using this machine is VERY HIGH |

## IDENTIFIED RISKS AND HAZARDS

Hazards that may arise when operating wood machinery include:

- moving and rotating parts (blades and bits, tool disintegration)

- movement of the workpiece

- inhalation of dust particles

- electrocution from power faults or faulty equipment

- ejection of waste materials from cutting blades

- hand and finger injuries from rotating blades

- squash, pinch and crush injuries

### PRE-OPERATIONAL SAFETY

- The isolating switch should be in the OFF position.  The machine must be isolated from the main electricity supply when not in use.

- Cutters should be tight in the cutter block, sharp, without chips, gaps or cracks.

- The flutes on the infeed roller should not be clogged with resinous matter or other residue such as wood particles. The outfeed rollers should be clean.

- The table should be clean and free of chips and resinous matter such as gum.

- The anti-friction rollers should rotate freely without obstructions.

- The guards and dust extraction cover should be properly fitted and secure.

#### OPERATING SAFETY PRECAUTIONS

- Always keep the hands clear of the cutter block.

- Allow the cutter block to reach full speed before feeding material into the thicknesser.

- Never look into the feed opening while the cutter block is rotating and don't clean the table while the cutter block is rotating.

- Don't feed timber that varies significantly in thickness into the thicknesser as kickback may occur.

- Don't stand in line with the timber being fed in case of kickback.

- Don't lower the table when a piece of timber won't feed as kickback may occur.