# SAFETY OPERATING PROCEDURE

Tractor

DO NOT use this machine unless a teacher has instructed

you in its safe use and operation and has given permission.

### PRE-OPERATIONAL SAFETY CHECKS

- Ensure that the seatbelt, Roll Over Protective Structure (ROPS), Falling Objects Protective Structure (FOPS) (where fitted) and Power Take-Off (PTO) guard are in sound condition.

- Faulty equipment must not be used. Report suspect machinery immediately.

- Check the 3-point linkage, pneumatic and hydraulic systems are functioning.

- Use only implements that meet the specifications listed in the vehicle operation manual.

- Ensure tractor driver is trained and competent and if driving on public roads, appropriately licensed.

- If the tractor is used on public roads, ensure that all lights and warning devices are operational and the vehicle is registered.

#### OPERATIONAL SAFETY CHECKS

- Never start or operate levers from anywhere other than the seat.

- Before starting the tractor, ensure all levers are in their neutral positions, the parking brake is engaged and the clutch and PTO are disengaged.

- Do not operate or idle engine in a non-ventilated area.

- Pull only from the drawbar or hitch.

- Drive at speed slow enough to keep control over unexpected hazards.

- Do not operate near ditches, holes or embankments, which may collapse under the tractor’s weight.

- Always reverse when going up a steep slope. Avoid slopes that are too steep for safe operation.

- Do not dismount from a tractor while the engine is running unless the vehicle has completely stopped, the transmission is in park position and the parking brake is fully engaged.

- Ensure that no person or animal is endangered when operating the equipment.

- Ensure bucket (if fitted) is raised above line of site.

- When stopping the tractor:

- Park on even ground, disengage the PTO and lower all implements.

- Place all control levers in their neutral positions, apply the parking brake, turn off the engine and remove the keys.

- Ensure the tractor has come to a complete stop before dismounting.

#### HOUSEKEEPING

- Clean away any foreign material, debris from in and around engine and implement parts.

- Keep the work area or implement shed in a clean and tidy condition.

## POTENTIAL HAZARDS

(	Entanglement in PTO 	(	Noise 	(	Rollover