# SAFE OPERATING PROCEDURE

Wood Burner

|  | DO NOT use this appliance unless you have had instruction and training in its safe use and operation. Teacher permission MUST be given to operate this appliance. |
| --- | --- |
| The risk of injury when using this machine is LOW |

## IDENTIFIED RISKS AND HAZARDS

Hazards that may be encountered when using the wood burner include:

- burns from the tip

- fire from protective paper catching alight

- electrical faults

Burns can occur from touching hot metal parts on the heater. Use caution when handling the heater - especially when packing away after a bending operation.

## PRE-OPERATIONAL SAFETY

- Always check that the heater and its electrical cord are in good working order.

- Check all adjustments and settings carefully before commencing any heating

operation.

- Make sure the heater is turned off before making adjustments.

- The work area should be clean and free of equipment, rubbish and other obstacles.

- Adjust the temperature correctly.  Consult labels for manufacturer’s suggestions.

OPERATING SAFETY PRECAUTIONS

- Allow the heater to reach maximum temperature before applying the workpiece.

- Keep hands well away from the tip when operating.

- Never leave the heater unattended when turned on.

- Keep fingers away from the heater's resting plate whilst heating.