# SAFE OPERATING PROCEDURE

Wood Turning Lathe

|  | DO NOT use this machine unless you have had instruction and training in its safe use and operation. Teacher permission MUST be given to operate this machine. |
| --- | --- |
| The risk of injury when using this machine is SUBSTANTIAL |

## IDENTIFIED RISKS AND HAZARDS

Hazards that may arise when operating fixed machinery include:

- movement of the workpiece

- inhalation of dust particles

- electrocution from power faults or faulty equipment

- ejection of waste materials

- hand and finger injuries from rotating workpiece, spindles or pulleys

- squash, pinch and crush injuries

- swarf being ejected from machines

### PRE-OPERATIONAL SAFETY

- The isolating switch should be in the OFF position.

- The lathe bed should be free of all material and tools.

- Check that the dust extraction system is working properly.

- The work area should be clean and free of sawdust and other obstacles.

- Ensure all guards are correctly fitted and secured.

- Check that the speed of the lathe is correct for diameter of the workpiece and check that the cone pulley belt has been installed properly.

#### OPERATING SAFETY PRECAUTIONS

- Ensure that the workpiece is secure between the live centre and the dead centre

- Allow the lathe to reach maximum speed before applying the turning tool.

- Keep the hands well away from the workpiece when the lathe is running.

- Ensure that all of the accessories are secure and the turning chisels are sharp.

- Position the tool rest at the correct height and distance from the work piece.

- Revolve the workpiece by had once or twice before starting the lathe to check the correct positioning of the tool rest and the mounting of the spur (live) centre and dead centre.

- Stop the wood lathe and make sure the workpiece is stationary when checking measurements.

- Never leave the wood lathe unattended when it is running.